## Slide 1
LG 부트캠프 8기 프로젝트 C반 1팀
Signal EQ & Analyzer
RTOS, Sw2Pjt
최준하, 장다운, 이승종
프로젝트 결과보고서

## Slide 2
프로젝트 목표 및 결과
개발 목표
핵심 기술
결과 분석 및 기대 효과
향후 연구 과제

## Slide 3
1. 프로젝트 목표 및 결과
＂Signal의 주파수를 분석하여 시각화”
＂주파수 밴드를 맞춤 제작하여
Signal Processing”
프로젝트 주제: Signal EQ & Analyzer

## Slide 4
2. 개발 목표
OS Components 목표
커널을 가볍게 설계하여
안정성을 유지하고,
응용 프로그램에 필요한 메모리와 CPU 자원을 최적화하여 여유 확보.
APP Components 목표
C++를 사용하여 OOP 기반으로 설계하고 구현함으로써
유지보수성과 확장성을 확보,
FPU 없이 MCU만으로 DSP 기능을 구현하여
성능을 최적화.

## Slide 5
3. 핵심 기술
RTOS
Task Manager
Queue
Gate Keeper
Mutex
Interrupts Lock Manager
Signal
DSP
FFT (Fast Fourier Transform)
Filter (LPF, HPF, BPF)
머신러닝을 통한 필터 최적화
팀워크
현업에서부터 한 팀

## Slide 6
3. 핵심 기술
OS Kernel Components
Living
RTOS
Task
Manager
Queue
Mutex
Free Task Pool: Stack
Ready List Pool:
Circular Doubly Linked List
Blocked List Pool:
Circular Doubly Linked List
*유지보수성: OOP, 책임분리, Self
Interrupts Lock Manager
Scoped
Lock
*안정성: RAII, Tail, Counter

## Slide 7
3. 핵심 기술
*효율성: Task별 관리
OS Kernel Components
Task 1
Task 2
Interrupts 1
Gate Keeper
전용 메일함
(Queue)
Gate Keeper
LCD
*안정성: Gate Keeper
Task
Manager

## Slide 8
3. 핵심 기술
OS Kernel Components
Signal Task
Uart Task
DSP Task
Mutex
Memory
Signal
UART Task
DSP Done
GUI
UART Send
(Filtered Data, Filter Type)
Blocked
DSP Task
DSP Done
Running

## Slide 9
3. 핵심 기술
Application Components - DSP
DSP
FFT
Filtering
Twiddle Factor LookUp Table
CMSIS-DSP 모방
Loop 최적화 (Unrolling)

## Slide 10
3. 핵심 기술
Application Components - DSP
IIR (ButterWorth 4th)
FIR (Hanning Window 32th)
필터선별
Filter Kernel Design
Bayesian 최적화
*복잡한 요구조건 대응

## Slide 11
3. 핵심 기술
Application Components – GUI
Signal 시각화
Filtered Signal 시각화 (보드에서 연산 후 UART로 전송)
UART 통신 Log
Signal Preset 선택
Filter Type 선택

## Slide 12
3. 핵심 기술
Application – Filter 특성 (BPF)
IIR Filter
FIR Filter

## Slide 13
4. 결과 분석 및 기대 효과
결과 분석
기대 효과
구현성
2. OS 안정성
3. Application 성능
- Analyzer, 3-band(LPF,HPF,BPF)
- SW인정시험 통과(자체)
- 실시간 Filtering
- Filtering 성능 준수 & GUI확인
원가 개선
2. 맞춤 제작
- FPU탑재 모델 Cortex-M33 대비 절반 가격인 Cortex-M3
- 고객에 최적화된 맞춤 커널로 만족도 상승

## Slide 14
5. 향후 연구 과제
ADC/DAC를 확보한 후, 실시간 음악 데이터를 입력받아 Processing하고, 오디오 출력을 통해 결과물을 확인
Adaptive한 밴드 조절 기능을 적용하여 원 EQ의 기능 추가
Cortex-M0에서 구현 가능하도록 최적화 하여 원가개선

## Slide 15
Thank You
Q&A