## Slide 1
LG 부트캠프 8기 프로젝트 RTOS반 SW2PJT팀
Signal Analyzer & Filter
RTOS, SW2PJT
최준하, 장다운, 이승종
프로젝트 결과보고서

## Slide 2
프로젝트 개관
개발 목표
핵심 기술
결과

## Slide 3
1. 프로젝트 개관
프로젝트 목표: Kernel 구현

## Slide 4
1. 프로젝트 개관
＂Signal의 주파수를 분석하여 시각화”
”실시간 Digital Signal Processing”
프로젝트 주제: Signal Analyzer & Filter

## Slide 5
2. 개발 목표
OS Components 목표
안정성
APP Components 목표
FPU 없이 MCU만으로 DSP 기능을 구현
(Cortex-m3가 m33 대비 절반 가격)

## Slide 6
3. 핵심 기술
RTOS
Task Manager
Queue
Gate Keeper
Mutex
Interrupts Lock Manager
Signal
DSP
FFT (Fast Fourier Transform)
Filter (LPF, HPF, BPF)
머신러닝을 통한 필터 최적화

## Slide 7
3. 핵심 기술
System
Living
RTOS
Task
Manager
Queue
Mutex
Free Task Pool
Ready List Pool
Blocked List Pool
*유지보수성: OOP, 책임분리
DSP
FFT
Filter

## Slide 8
3. 핵심 기술
OS Components_자원관리
Signal Task
Uart Task
DSP Task
Mutex
Memory
Task
인터럽트
Keeper
전용 메일함
(Queue)
Gate Keeper
LCD
*안정성: Gate Keeper
Task

## Slide 9
3. 핵심 기술
OS Components_Profile
Interrupts Lock Manager
Scoped Lock
*안정성: RAII, Tail, Counter
Keyword
Inline assembly
R0 = self
함수호출규약

## Slide 10
3. 핵심 기술
Application Components - DSP
DSP
FFT
Filtering
Twiddle Factor LookUp Table
CMSIS-DSP / MATLAB 오마쥬
ARM_MATH로 산술 연산 최적화

## Slide 11
3. 핵심 기술
Application Components – 요구조건 사고실험
로봇 피드백 제어 시스템
저역 Cutoff Frequency = 600
고역 Cutoff Frequency = 1200
저역 필터 위상 지연 최소

## Slide 12
3. 핵심 기술
Application Components - DSP
IIR (ButterWorth 4th)
FIR (Hamming Window 32th)
Filter Kernel Design
Bayesian 최적화
Heuristic

## Slide 13
4. 결과
Application – DSP 연산시간
 | FIR | IIR
LPF | 13 | 7
HPF | 12 | 7
BPF | 20 | 10
FFT Length 128, SampleRate:4000
단위: ms

## Slide 14
4. 결과
Application – Filter 특성(LPF)
IIR Filter
FIR Filter

## Slide 15
4. 결과
Application – Filter 특성(HPF)
IIR Filter
FIR Filter

## Slide 16
4. 결과
Application Components – GUI
FIR LPF
FIR HPF

## Slide 17
4. 결과
Normal
FIR LPF
FIR HPF
FIR BPF

## Slide 18
Thank You
Q&A